Exact channel solutions with viscosity, resistivity and cooling
P. Lesaffre
S. Balbus
ENS/LRA
Thanks: S. Fromang, L. Silvers

---
Outline
Shearing sheet equations
Linear Solutions
Code design & Benchmarks
Numerical viscosity and resistivity

---
Motivation:
more microphysics in codes
Example: study of active and dead phase separation in a local simulation with temperature-dependent resistivity.

---
(1) SHEARING SHEET
Equations

---
(2) Trial Solution : steady flow + vertical Fourier mode

---
Incompressible solution

---
Vertical Magnetic field

---
“Linear” Cooling
(Equivalent to the leading Taylor expansion w.r.t. temperature of the net heating/cooling function)

---
Total pressure gradient
Last remaining non linear term

---
Total pressure evolution
Spatial constant, exponential in time
Need to be zero
=> s has to be a root of Q and the dispersion relation of the system at the same time
=> we get 1 constraint on the parameters n, h, A, W, w and a

---
Solutions
Recover torsional Alfvén waves in absence of shear
Generally are standing waves, possibly growing, ie: Channel solutions
Possible extensions:
  - thermal conduction
  - non zero radial wave numbers

---
Internal energy equation (Stone & Norman 1992)
Total energy equation (Turner et al. 2003; Hirose et al. 2006)
(3) Code design & Benchmarks
Start with ZEUS3D

---
Benchmark:
Torsional Alfvén waves
A torsional Alfvén wave
after 3 oscillations
(see Turner et al. 2003)
Total energy
scheme
Analytic
Internal energy
scheme
The internal energy scheme distorts the wave

---
Benchmark:
with resistivity and viscosity
A torsional Alfvén wave
after 7.2 periods
Analytic
Total energy
scheme
Internal energy
scheme
Adding some physical viscosity and resistivity improves the internal energy scheme.

---
Benchmark: MRI modes with resistivity (and cooling)
Resistivity is adjusted to satisfy total pressure homogeneity
The potential energy flux should better be computed along the transport step rather than associated with the Coriolis momentum source.
at Coriolis
force
at transport step
MRI standing mode after 8 orbits

---
(4) Measuring h and n
Viscosity
Viscosity
Resistivity
Resistivity
Scheme unstable !
h+n can be measured from the decay
h-n can be measured from the phase lag between velocity and magnetic field

---
Anistropy of
numerical dissipation
Dissipation depends upon leading wave number
Elongated pixels increase anisotropy
They also increase the total dissipation: not worth the resolution ?
Dependence on k linked to bottleneck effect ?

---
Conclusions
New benchmarks
ZEUS3D+...
Thermal stability of accretion disks
Next step: RAMSES-MHD with shearing box and resistivity
Parasitic instabilities with more physics

---
Why an elongated box ?
Parasitic instability (Goodman & Xu, 1998) peaks at ~ a third of the MRI most unstable mode.
1 box
2 boxes
4 boxes
6 boxes